## Slide 1: Day 2
Group Pi

## Slide 2: Subnet Mask

## Slide 3: Subnet Mask
To find the network number and broadcast number first convert the IP into binary. (Ignore the number after the slash for now)
192.168.2.42 / 24
192 . 168 . 2 . 42
11000000.10101000.0000010.00011000

## Slide 4: Subnet Mask
Then count over the amount of bits specified by the number following the slash.
192.168.2.42 / 24
1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 22 23 24
11000000.10101000.00000010|.00011000

## Slide 5: Subnet Mask
Replace the rest of the numbers with X’s.
1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 22 23 24
11000000.10101000.00000010|.00011000
11000000.10101000.00000010|.XXXXXXXX

## Slide 6: Subnet Mask
To find the network number replace all the X’s with zeros and convert back to decimal.
11000000.10101000.00000010|.XXXXXXXX
11000000.10101000.00000010.00000000
192 . 168 . 2 . 42
Network Number: 192.168.2.0

## Slide 7: Subnet Mask
To find the broadcast number replace all the X’s with ones and convert back to decimal.
11000000.10101000.00000010|.XXXXXXXX
11000000.10101000.00000010.111111111
192 . 168 . 2 . 255
Broadcast Number: 192.168.2.255

## Slide 8: Subnet Mask
To find the amount of viable IP’s take 2 and raise it to the power of 32 minus the net mask number and subtract two.
192.168.2.42 / 24
2^(32-24) = 2^8 = 256
256 - 2 = 254
Viable IP’s: 254

## Slide 9: Subnet Mask
The IP range is between the network number and the broadcast number(non-inclusive).
Network Number: 192.168.2.0
Broadcast Number: 192.168.2.255
Viable IP’s: 254

## Slide 10: Packet Tracer

## Slide 11: Setting Up a basic Network
To set up a simple network you need to add two routers, two switches, and two PC’s in this or a similar formation.

## Slide 12: Setting Up a basic Network
You add new components by clicking the category then clicking and dragging an item into the workspace.

## Slide 13: Setting Up a basic Network
After you have you need to connect everything. By using the same method drag cables out and click on a node. It will bring up a menus of ports to connect to. Choose a fast ethernet port, then repeat the process on another node to connect them.

## Slide 14: Setting Up a basic Network
Now you need to assign the computers IP’s. Double click to open a computer’s menu.
Then click Desktop.
Then IP Configuration.

## Slide 15: Setting Up a basic Network
Now you must enter a valid IP, Subnet Mask and Default Gateway.
Do this for both computers.

## Slide 16: Setting Up a basic Network
Now open the router menu, and click on the CLI tab.

## Slide 17: Setting Up a basic Network
Type these into the interface:
-en
-conf t
Each port must be configured so follow these commands for each port
-int fa<port>
-ip add <ip> <subnet>
-no shut
-exit

## Slide 18: Setting Up a basic Network
Now test the network by bring up the computer desktop again. Click on the Command Prompt. Then type ‘ping <address>’, address being a IP on the network. A reply indicates functionality.

## Slide 19: Setting Up DHCP
First setup the configuration like this by dragging and dropping the items you need from the menu below

## Slide 20: Setting Up DHCP
Next we need to add some hardware to the router so it can accept 3 inputs

## Slide 21: Setting Up DHCP
Now we configure the server as a DHCP server. Set the IP of the server itself as static in the global settings and on FastEthernet0.

## Slide 22: Setting Up DHCP
Use the command line interface to set the ips of the interfaces in the router

## Slide 23: Setting Up DHCP
Then we followed the directions from http://www.firewall.cx/cisco-technical-knowledgebase/cisco-routers/812-cisco-router-dhcp-config.html to set up the router to forward the DHCP from the server

## Slide 24: Setting Up DHCP
Then set the ip configuration of each pc to DHCP.

## Slide 25: Setting Up DHCP
And finally go to command prompt in a pc and type “ipconfig” and it should return the ip address it was given.

## Slide 26: Resources
Help From:
Resources on team server
Team Leaders
http://www.firewall.cx/cisco-technical-knowledgebase/cisco-routers/812-cisco-router-dhcp-config.html